## Slide 1: Automated Weld Path Generation Using Random Sample Consensus and Iterative Closest Point Workpiece Localization – DETC90082
Tristan Hill
Tennessee Technological University
Stephen Canfield
Tennessee Technological
University
Robert Shelton
Tennessee Technological
University

## Slide 2: Overview
Applications:
Background – Robotics and Automated Welding
Method – Workpiece Localization
Results - Simulated and Experimental
Conclusions – Applications and Future Work

## Slide 3: Robotics in Manufacturing
Benefits and Tradeoffs:
Efficiencies
Safety
Employment ?
Technologies:
Serial Manipulators
Parallel Manipulators
Mobile Robots
Vision and Sensing
Cobots and Safety Systems
Applications:
Welding
Painting
Applying Glue
Additive Manufacturing
Source: Wikipedia, Industrial Robot
Source: RTT, C.R. Weld

## Slide 4: Automated Welding and Tool Path Generation
The transformation from the manipulator base frame to the start point on the workpiece must be known.
Fixtures or Jigs
Vision and Sensing
Teaching
Automation requires control of tool pose typically achieved using a kinematic model and joint level control.
A spatial description of the desired task is required.
Manual programming
Teaching with Pendant or Hand
Computer Modeling

## Slide 5: Literature Review
Automation of welding has been a focus of robotics research for many years
Seam Tracking
Start Point Determination
Workpiece Localization
Image registration is a fundamental problem in computer vision and has been studied thoroughly. This field is changing rapidly with technological developments.
Sensing and Data Storage
Computational Abilities
Algorithms and Machine Learning

## Slide 6: Contribution
A process is shown which uses RANSAC and ICP for workpiece localization from a point cloud data containing outliers for a robotic welding application.

## Slide 7: Overview of Approach
The process consists of multiple stages.
Model Preparation
Workpiece CAD
Model Generation
Conversion to
Pointcloud
Workspace Sensing
Collection of
2D LiDAR Scans
Conversion to
Pointcloud
Path Generation
Weld Path Construction with LSPB
Projection to workpiece frame
Workpiece Localization
PassThrough + Voxel Filtering
RANSAC
Segmentation
ICP
Registration
1- Model Preparation
2 - Workspace Sensing
3 - Workpiece Localization
4 - Path Generation

## Slide 8: Model Preparation
Workspace Sensing
  the geometry of the workspace and the workpiece is defined based on the prescribed application. An ideal model of the workpiece is generated using CAD.
  Part models are first generated of the individual workpiece components which are then assembled to represent the workpiece.
Conversion to Point Cloud
  The 3D models are generated using standard CAD software can be convered to point clouds through uniform sampling and exported as .ply or other standard file formats
  The point cloud associated with the CAD model is known as the source point cloud.

## Slide 9: Workspace Sensing
Collection of 2D LiDAR Scans
  the workpiece is placed in the robot workspace by the operator in the proper relative orientation to be joined by a weldment.
  a sweeping motion of the arm is performed, and the workpiece and environment are scanned with the 2D LiDAR mounted on link 5 of the robot.
Conversion to Point Cloud
  data are transformed from the sensor frame link 5 to the base frame link 0 through the known robot kinematics and accumulated into a 3D point cloud with respect to the base frame.
  The point cloud associated with the LiDAR scan is known as the reference or target cloud.

## Slide 10: Workpiece Localization
PassThrough + Voxel Filtering
  The filtering process remove data points outside of the useable workspace
RANSAC Segmentation
  The segmentation process removes points inside the workspace that are not part of the workpiece
  This process must be adjusted for the specific workpiece geometry
ICP Registration
  the source point cloud derived from the CAD model is compared to the reduced reference cloud acquired from lidar in the sensing stage
  transformation between source and reference clouds is found using the iterative closest point algorithm (ICP), this transformation is interpreted as the pose of the workpiece.
  Iterative Closest Point relies on correspondence between points between data sets therefore it fails or converges slowly in the presence of outliers.

## Slide 11: Path Generation
Path construction with LSPB
Projection to workpiece frame
Orientation of the Torch
Pi+1
Oi,i+1
Pi+2
O1+1,i+2
Pi
n
t
RP
xWP
qw
x’
qR
zWP, z’
y’, y’’
xT
qw
qT
zT
qT
x0
y0
z0

## Slide 12: Implementation with ROS + PCL
This research has been implemented in ROS on Ubuntu Linux
  multi-threaded and distributed software framework for robotics applications.
The combination of 2D LiDAR scans into 3D point clouds was done using a custom ROS package scan2cloud based on ROS laser_geometry (https://github.com/thillRobot/scan2cloud.git)
The primary approach was implemented in a custom ROS package seam_detection that uses PCL for filtering, RANSAC, and (https://github.com/thillRobot/seam_detection.git)
Email: thill@tntech.edu for questions about code

## Slide 13: Simulation Results
The process was first completed on synthetic data. The source and reference clouds were both generated from CAD.
 | X | Y | Z
Expected Translation | 0.25 | 0.2 | 0.025
Measured Translation | 0.251347 | 0.19923 | 0.02436
Difference | -0.00134 | 0.00077 | 0.00064
 | Roll | Pitch | Yaw
Expected Rotation | 0.0 | 0.0 | 0.52360
Measured Rotation | -0.00918 | -0.00681 | 0.52759
Difference | 0.00918 | 0.00680 | -0.00399
FIGURE 6: SIMULATED APPLICATION – WORKPIECE REGISTRATION
FIGURE 5: SEGMENTATION TO REMOVE CLAMPS
FIGURE 4: SEGMENTATION TO REMOVE TABLE
TABLE 1: SIMULATION RESULTS – EXAMPLE APPLICATION

## Slide 14: Experimental Results
The approach was tested using a Aubo i5 cobot and an RPLiDAR A2 on a welding table courtesy of RTT – Robotic Technologies of Tennessee and Stephen Zuccaro.
FIGURE 10: EXPERIMENTAL EXAMPLE APPLICATION
FIGURE 5: SEGMENTATION TO REMOVE CLAMPS
FIGURE 4: SEGMENTATION TO REMOVE TABLE
FIGURE 3: BOUNDING BOX

## Slide 15: Experimental Results
 | X (m) | Y (m) | Z (m)
Expected Translation | 0.0 | -0.60960 | 0.02540
Measured Translation | 0.00893 | -0.60874 | 0.02003
Difference | -0.00893 | -0.00086 | 0.00537
 | Roll (rad) | Pitch (rad) | Yaw (rad)
Expected Rotation | 0.0 | 0.0 | 0.0
Measured Rotation | -0.00493 | -0.00071 | 0.019938
Difference | 0.00493 | 0.00071 | -0.00071
 | X (m) | Y (m) | Z (m)
Expected Translation | 0.10160 | -0.60960 | 0.02540
Measured Translation | 0.10840 | -0.61096 | 0.02034
Difference | -0.00680 | 0.00136 | 0.00506
 | Roll (rad) | Pitch (rad) | Yaw (rad)
Expected Rotation | 0.0 | 0.0 | 0.785
Measured Rotation | -0.00457 | 0.02186 | 0.79461
Difference | 0.00457 | -0.02186 | -0.00921293
TABLE 3: EXPERIMENTAL RESULTS - EXAMPLE APPLICATION
TABLE 2: EXPERIMENTAL RESULTS – LIDAR CALIBRATION
FIGURE 14: EXAMPLE APPLICATION – WORKPIECE REGISTRATION

## Slide 16: Conclusion
sfghsfghsfgh
asdfazsdf